# Network Boot Your Raspberry Pi
This tutorial is written to explain how to set up a simple DHCP/TFTP server which will allow you to boot a Raspberry Pi 3 from the network. The tutorial assumes that you have an existing home network, and that you want to use a Raspberry Pi for the server. You will need a second Raspberry Pi 3 as a client to be booted. Only one SD card is needed because the client will be booted from the server after the initial client configuration.
## Client configuration
Before a Raspberry Pi will network boot, it needs to be booted from an SD card with a config option to enable USB boot mode. This will set a bit in the OTP (One Time Programmable) memory in the Raspberry Pi SoC that enables network booting. Once this is done, the SD card is no longer required.
Install Raspbian Lite (or Raspbian with PIXEL) on the SD card in the normal way See here.
### Program USB Boot Mode
First, prepare the /boot directory with the latest boot files:
sudo apt-get update && sudo apt-get upgrade
Now, enable USB boot mode with the following command:
echo program_usb_boot_mode=1 | sudo tee -a /boot/config.txt
This adds program_usb_boot_mode=1 to the end of /boot/config.txt. Reboot the Raspberry Pi with sudo reboot. Once the client Raspberry Pi has rebooted, check that the OTP has been programmed with:
$ vcgencmd otp_dump | grep 17:
17:3020000a
Ensure the output 0x3020000a is correct.
The client configuration is almost done. The final thing to do is to remove the program_usb_boot_mode line from config.txt (make sure there is no blank line at the end). You can do this with sudo nano /boot/config.txt, for example. Finally, shut the client Raspberry Pi down with sudo poweroff.
## Server configuration
Plug the SD card into the server Raspberry Pi. Boot the server. Before you do anything else, make sure you have run sudo raspi-config and expanded the root filesystem to take up the entire SD card.
The client Raspberry Pi will need a root filesystem to boot off, so before we do anything else on the server, we're going to make a full copy of its filesystem and put it in a directory called /nfs/client1.
sudo mkdir -p /nfs/client1
sudo apt-get install rsync
sudo rsync -xa --progress --exclude /nfs / /nfs/client1
Regenerate SSH host keys on the client filesystem by chrooting into it:
cd /nfs/client1
sudo mount --bind /dev dev
sudo mount --bind /sys sys
sudo mount --bind /proc proc
sudo chroot .
rm /etc/ssh/ssh_host_*
dpkg-reconfigure openssh-server
exit
sudo umount dev
sudo umount sys
sudo umount proc
Find the settings of your local network. You need to find the address of your router (or gateway), which can be done with:
ip route | grep default | awk '{print $3}'
Then run:
ip -4 addr show dev eth0 | grep inet
which should give an output like:
inet 10.42.0.211/24 brd 10.42.0.255 scope global eth0
The first address is the IP address of your server Raspberry Pi on the network, and the part after the slash is the network size. It is highly likely that yours will be a /24. Also note the brd (broadcast) address of the network. Note down the output of the previous command, which will contain the IP address of the Raspberry Pi and the broadcast address of the network.
Finally, note down the address of your DNS server, which is the same address as your gateway. You can find this with:
cat /etc/resolv.conf
Configure a static network address on your server Raspberry Pi by with sudo nano /etc/network/interfaces (where you replace nano with an editor of your choice). Change the line, iface eth0 inet manual so that the address is the first address from the command before last, the netmask address as 255.255.255.0 and the gateway address as the number received from the last command.
auto eth0
iface eth0 inet static
        address 10.42.0.211
        netmask 255.255.255.0
        gateway 10.42.0.1
Disable the DHCP client daemon and switch to standard Debian networking:
sudo systemctl disable dhcpcd
sudo systemctl enable networking
Reboot for the changes to take effect:
sudo reboot
At this point, you won't have working DNS, so you'll need to add the server you noted down before to /etc/resolv.conf. Do this by using the following command, where the IP address is that of the gateway address you found before.
echo "nameserver 10.42.0.1" | sudo tee -a /etc/resolv.conf
Make the file immutable (because otherwise dnsmasq will interfere) with the following command:
sudo chattr +i /etc/resolv.conf
Install software we need:
sudo apt-get update
sudo apt-get install dnsmasq tcpdump
Stop dnsmasq breaking DNS resolving:
sudo rm /etc/resolvconf/update.d/dnsmasq
sudo reboot
Now start tcpdump so you can search for DHCP packets from the client Raspberry Pi:
sudo tcpdump -i eth0 port bootpc
Connect the client Raspberry Pi to your network and power it on. Check that the LEDs illuminate on the client after around 10 seconds, then you should get a packet from the client "DHCP/BOOTP, Request from ..."
IP 0.0.0.0.bootpc > 255.255.255.255.bootps: BOOTP/DHCP, Request from b8:27:eb...
Now we need to modify the dnsmasq configuration to enable DHCP to reply to the device. Press CTRL+C on the keyboard to exit the tcpdump program, then type the following:
echo | sudo tee /etc/dnsmasq.conf
sudo nano /etc/dnsmasq.conf
Then replace the contents of dnsmasq.conf with:
port=0
dhcp-range=10.42.0.255,proxy
log-dhcp
enable-tftp
tftp-root=/tftpboot
pxe-service=0,"Raspberry Pi Boot"
Where the first address of the dhcp-range line is, use the broadcast address you noted down earlier.
Now create a /tftpboot directory:
sudo mkdir /tftpboot
sudo chmod 777 /tftpboot
sudo systemctl enable dnsmasq.service
sudo systemctl restart dnsmasq.service
Now monitor the dnsmasq log:
tail -F /var/log/daemon.log
You should see something like this:
raspberrypi dnsmasq-tftp[1903]: file /tftpboot/bootcode.bin not found
Next, you will need to copy bootcode.bin and start.elf into the /tftpboot directory. You should be able to do this by copying the files from /boot, since these are the right ones. We need a kernel, so we might as well copy the entire boot directory.
First, use Ctrl+C to exit the monitoring state. Then type the following:
cp -r /boot/* /tftpboot
Restart dnsmasq for good measure:
sudo systemctl restart dnsmasq
### Set up NFS root
This should now allow your Raspberry Pi to boot through until it tries to load a root filesystem (which it doesn't have). All we have to do to get this working is to export the /nfs/client1 filesystem we created earlier.
sudo apt-get install nfs-kernel-server
echo "/nfs/client1 *(rw,sync,no_subtree_check,no_root_squash)" | sudo tee -a /etc/exports
sudo systemctl enable rpcbind
sudo systemctl restart rpcbind
sudo systemctl enable nfs-kernel-server
sudo systemctl restart nfs-kernel-server
Edit /tftpboot/cmdline.txt and from root= onwards, and replace it with:
root=/dev/nfs nfsroot=10.42.0.211:/nfs/client1,vers=3 rw ip=dhcp rootwait elevator=deadline
You should substitute the IP address here with the IP address you have noted down.
Finally, edit /nfs/client1/etc/fstab and remove the /dev/mmcblkp1 and p2 lines (only proc should be left).
Good luck! If it doesn't boot on the first attempt, keep trying. It can take a minute or so for the Raspberry Pi to boot, so be patient.